PRCD (Type: MS-4013) OPERATING INSTRUCTIONS

Caution: please read the user manual carefully before use

1, Technical equipment

- Red indicator

Protection active

- Reset

Activates the protection

- T

Activate the test function

2, TEST BEFOR USE

WARNING

1). Directly plug into fixed socket，

2). Press “RESET” button：indicator should be “ON”;

3). Press “T” button：indicator should be “off”;

4). Press “RESET” button for use. Do not use if test failed

3, Advice

1: For indoor use only.

2: The maximum value of the mean daily ambient temperature is +35 °C and between –5°C to 40°C.

3: Altitude: Not exceeding 2 000 m

4: Relative humidity (maximum value at 40°C): 50%

5: Frequency: Reference value is in ±5 % (250V~ 50Hz, 10A)

6: External magnetic field: Not exceeding five times the earth’s magnetic field in any direction. It also Means the device should not be used in the proximity of a strong magnetic field.

7: Sinusoidal wave distortion: Not exceeding 5 %

8: After the item 1)-4), the device is ready for use. The device shall not be used if it fails to operate correctly in accordance with the test sequence listed above. In this case, please unplug the device to outlet.

9: Please make sure the device can work normally by conducting the above operation sequence at first to protect against unexpected electric leakage hazard before use. Don’t misuse such as dropping, immersion, etc.

10: In case of electric leakage, the device will automatically shut off the power supply and prevent electricity reaching human bodies.

11: Seek advice from manufacturer or responsible vender or a competent electrician for solution if the device repeatedly trips with an appliance connected or if it fails to pass the test sequence listed above.

12: Misuse of electricity can be dangerous, the use of a PRCD cannot be regarded as substitute for basic electrical safety, please unplug the PRCD to achieve isolation.

4, Technical data

Power supply            250V～50HZ

Rated current                10A

Rated output               2500W

Trip leakage current          30mA

Trip time                  ﹤30mS

Type of protection             IP40

Distributed by:

Electus Distrubution Pty Ltd.

320 Victoria Road,Rydalmere,NSW 2116 Australia.

Phone:1300 738 555

Facsimile:1300 738 500

www.electusdistribution.com.au