LED Party or Stage Lighting Kit with Stand & Controller

User Manual

- Specification:

Input: AC240V, 50Hz;

LED：Ø10 LED, Each par Can has 145pcs LEDs :( 49R, 48G, 48B),

Control Mode: Sound Activated, Automatic, DMX512.

Power Consumption: 100W

- Installation:

Please unpack the bag and find the 4pcs par cans, please hang the 4pcs par cans by screws to the main stand, and adjust the par can to a suitable angle as you like.

Connect signal wire: plug one end of the signal wire into INPUT socket at the back of the projector system. The other end into OUTPUT which is signal output of DMX512.

To connect the foot controller, Plug the signal cable from the OUTPUT socket

of the controller to the CONTROL OUT socket on the back of the unit. The DMX cable needs to be unplugged in order for the foot control mode to operate.

- Operation and Function:

Menu display function

| Display | Function |
| --- | --- |
| ADDR(DMX address set up) | 1-512 |
| SLND(Master and Slave set up) | NAST(Master) |
|  | SLAV(Slave) |
| CHND(Channel Mode set up) | 4CH/15CH |
| SHND(Program set up) | SH 0…….SH12/FADE（SP 1……SP 8） |
| COLO(Colour set up) | COL1…….COL9 |
|  | NANV | R:0---255 |
|  |  | G: 0---255 |
|  |  | B: 0---255 |
| LED(background light set up) | ON/OFF |
| DISP(Positive & negative set up) | ON/OFF |
| TEST(Colour Auto-Test) | Colour Auto-Test |
| FHNS | Use time |

DMX Channel Function

4 DMX Channel:

| Channel | Channel values | Function |
| --- | --- | --- |
| 1channel | 0-------255 | Red light turns on, brightness from low to high |
| 2channel | 0-------255 | Green light turns on, brightness from low to high |
| 3channel | 0-------255 | Blue light turns on, brightness from low to high |
| 4channel | 0------190 | brightness from low to high |
|  | 191-- 200 | Sound Control |
|  | 201---247 | Flash frequently，from slow to fast |
|  | 248----255 | All lights turned on |

15DMX Channel:

| 1par | 1channel | 0 | light closed |
| --- | --- | --- | --- |
|  |  | 1-255 | Red light turns on, brightness from low to high |
|  | 2 channel | 0 | light closed |
|  |  | 1-255 | Green lasting lighted，From dark to bright |
|  | 3 channel | 0 | light closed |
|  |  | 01/01/55 | Blue light turns on，brightness from low to high |
| 2par | 4channel | 0 | light closed |
|  |  | 1-255 | Red light turns on, brightness from low to high |
|  | 5channel | 0 | light closed |
|  |  | 1-255 | Green light turns on, brightness from low to high |
|  | 6channel | 0 | light closed |
|  |  | 1-255 | Blue light turns on，brightness from low to high |
| 3par | 7channel | 0 | light closed |
|  |  | 1-255 | Red light turns on, brightness from low to high |
|  | 8channel | 0 | light closed |
|  |  | 1-255 | Green light turns on, brightness from low to high |
|  | 9channel | 0 | light closed |
|  |  | 1-255 | Blue light turns on，brightness from low to high |
| 4par | 10channel | 0 | light closed |
|  |  | 1-255 | Red light turns on, brightness from low to high |
|  | 11channel | 0 | light closed |
|  |  | 1-255 | Green light turns on, brightness from low to high |
|  | 12channel | 0 | light closed |
|  |  | 1-255 | Blue light turns on，brightness from low to high |
|  | 13 channel | 0 | light closed |
|  |  | 1-255 | General dimmer brightness from low to high |
|  | 14 channel | 0 | light c light closed |
|  |  | 1-255 | Flashes brightness from low to high |
|  | 15 channel | 0-5 | light closed |
|  |  | 6-100 | Colour fade(speed is from slow to fast) |
|  |  | 101-200 | Colour Auto-change(speed is from slow to fast) |
|  |  | 201-255 | Sound control |

Foot Controller

| STOP | Triggered once suspended(light closed), the second to restore the current state |
| --- | --- |
| MODE | Trigger one time for the selection of effects(SH1…SH12 FOR CHOOSE) |
|  | Trigger two times to choose the effect of the selected(FADE) |
|  | Trigger three times to choose the colour( COL1……COL9 ) NANV |
|  | Trigger four times for Sound control (SH 0) |
| UP | Changes through the different modes when pressed. |
| FULL | All PAR Lights will be lit up |

Note: If you change modes while set up in the foot controller mode, you need to hold down one of the 4 buttons down for 2 seconds. Doesnt matter which button you hold down in order to bring the foot control mode back otherwise it will not work.

- Maintenance

- Please make sure the power voltage is in accordance with the required power input of this unit.

- Please make sure the installation position is flat to make sure the lighting fixture stands firmly and all the four par lights are hanging on the same horizontal level.

- Please make sure the installation position is of good ventilation and has less humidity, and keep away from flammable and explosive objects.

- Don’t look into the light source directly to avoid hurting your eyes.