|  | SPECIFICATION | PAGE：1/5 |
| --- | --- | --- |
| PRODUCT SPECIFICATION ITEM ：DC MOTOR REMARKS： 1）This specification applies to the DC motor to be supplied to you. 2）We made this MOTOR SPECIFICATION is just for your conference. 3）When defective performance is occurred mutual discussions shall be made in accordance with SPECIFICATION FOR APPROVAL to resolve matter. 4）Please note that it is your responsibility to ensure that the motor can satisfy the requirements of your application. |
| DESIGN | CHECK | APPROVAL | 3 |  |  |
|  |  |  | 2 |  |  |
|  | SPECIFICATION | PAGE：2/5 |
| 1.Standard Operating Conditions: 标准运行条件 1-1.Rated Voltage 6.0 V DC constant 额定电压 1-2.Operating Voltage Range 5.0 ～ 9.0V DC at motor terminals 工作电压范围 1-3.Rated Load 100g.cm 额定负载 1-4.Direction of Rotation CCW when viewed from output shaft side. 旋转方向 CCW：从输出轴端看为逆时针 1-5.Motor Position All direction of protruded shaft 摆放位置 伸出轴的任意方向 1-6.Operating Temperature Range -5℃ ～ +50℃ 工作温度范围 2.Measuring Conditions: 测量条件 2-1.Motor Position Horizontally or Vertical 电机位置 水平或垂直。 2-2.Power Supply Regulated power supply which assures 电 源 unquestionable measurement 经过调节的直流稳压电源以确保无问题测量。 2-3.Environment Temperature and Humidity 环境温度与相对湿度 2-4.Unless otherwise specified, rated voltage to be applied. 除非特别注明，使用额定电压。 |
| DESIGN | CHECK | APPROVAL | 3 |  | 365SA-6V |
|  |  |  | NO. | DATE |  |
|  | SPECIFICATION | PAGE：3/5 |
| 3. Electrical characteristics 电气参数 3-1.No-load Speed 13500 ±10% rpm 空载转速 3-2.No-load Current 0.4 A Max 空载电流 3-3.Rated Speed 10000 ±10% rpm 额定转速 3-4.Rated Current 1.8 A Max 额定电流 3-5.Stall Torque 350 g.cm Min 堵转力矩 3-6.Reference Characteristic Curve See spec No.：RS-365SA-6V 参考特性曲线 4. Mechanical Structure and Character: 机械特性 4-1.Appearance No remarkable deformation and/or superficial defects. 外 观 表面无明显变形或缺陷。 4-2.Dimension As per dimensional drawing No.：RS-365SA-6V 外形图 符合尺寸图纸No.：RS-365SA-6V 4-3.Weights 50 g (Approx) 重 量 4-4.Shaft End Play 0.3mm Max 轴端间隙 4-5.Shaft T.I.R 0.02mm (max) at2/3 of output shaft side 轴径向跳动 and measured by dial gauge. 使用刻度表在轴端2/3处测量。 4-6.Mechanical Noise 机械噪音 50dB Max （测试仪器距电机300MM） 4-7.Vibration To be set up with mutual consent. 振 动 达到双方同意的标准。(封样) |
| DESIGN | CHECK | APPROVAL | 3 |  |  |
|  |  |  | 2 |  |  |
|  |  |  | 1 |  |  |
|  |  |  | NO. | DATE |  |
|  | SPECIFICATION | PAGE：4/5 |
| 5. Motor life test: 寿命试验 5-2.Voltage 6.0 V DC 电 压 5-3.Load 80g.cm 负 载 5-4.Environment 25℃±5℃ / 65%±20%RH 测试环境 5-5.Duty Cycle As sketched below. 测试周期 如下图所示 Life end defined as follows: 按如下状态确定寿命终结： When current is over ±30% against the initial figure. 电流与初始状态下的电流有±30%的差异。 2）When speed is beyond ±30% against the initial figure. 转速与初始状态下的转速有±30%的差异。 When motor is unquestionable recognized as unusable. 电机被明显确认为不可使用。 5-6.Life Expectancy: 800Hrs MIN 期望寿命 6. Storage 贮 存 6-1.Storage Temperature -20℃ ~ 70℃. 储存温度 6-2.Storage Relative Humidity 10% ~ 90%. 储存湿度 6-3.Keep dry, avoid storing in high temperature、high humidity or corrosive gas environment. 保持干燥，避免放置在高温、潮湿及有腐蚀性气体的环境中。 |
| DESIGN | CHECK | APPROVAL | 3 |  |  |
|  |  |  | 2 |  |  |
|  |  |  | 1 |  |  |
|  |  |  | NO. | DATE |  |

|  | SPECIFICATION | PAGE：5/5 |
| --- | --- | --- |
| 7. CAUTIONS： 注意事项 7-1.Since the performance of the motor is affected by environmental temperature, condition be give to keep it away from out of range. 环境温度条件对马达性能有极大影响，请在本技术指标范围内使用马达。 7-2.It is not allowed to operate in the high temperature with high humidity or in the rust or in the circumstance where the substances generating a harmful gas such as low molecular Siloxane, syan, formalin ,quick-dry glue or the corrosive gas such as H2S, SO2, XO2, Cl, exist. 避免在高温、高湿及与腐蚀液体、气体接触。 7-3. Do not give direct shock to the motor. 应避免直接碰撞马达。 8. REMARK： 备 注 8-1.Proper performance does not be guaranteed if the used in excess of specified value then indicated in the specifications. 当使用超出本规格书的指标范围，不能保证产品性能。 8-2.Any revision and addition to the specification shall be made after mutual discussion and agreement. 本规格书在双方协商后可进行调整与增加。 8-3.In case those motors returned to us comply with the characteristics this technical specification, We are not liable to repair the motors free of charge. 为避免合格产品退回我司，我司不为客户提供备份。 8-4.When infects are found for the motors duly approved by your incoming inspection, the defective motors shall be returned to us together with descriptions of the faults. We are to accept such motors only if the faults for each motors are clearly mentioned. 贵司在IQC检查中发现有瑕疵产品，请注明原因并退回， 我司不接受没有任何标注的产品。 |
| DESIGN | CHECK | APPROVAL | 3 |  |  |
|  |  |  | 2 |  |  |

# Text boxes

The test is made in principle at the

Temperature　between 10℃and30℃,and

at relative Humidity　between 30%and

95%, If the test result is　questionable,

it shall be judged from the test made

at JIS Standard Testing Condition

(20±2℃,65%±5%RH).

该试验原则上在温度为10℃~30℃之间、相对

湿度在30%~95%之间进行。如果对试验结果有

疑问，则应根据JIS标准试验条件下（20±2℃,

65%±5%相对湿度）进行的试验进行判断。